## Slide 1: Hydrogen Lyman-alpha Imager (HI)
Kazuo Yoshioka, Go, Murakami, Masaki, Kuwabara,
Makoto Taguchi, Shingo Kameda Ichiro Yoshikawa, and HI team
2022.07.08 CI Oxford MTG
HI (baffle)
NAC (baffle)
PS-ION
HI BBM

## Slide 2: Block diagram and specifications
Cassegrain-type optics
Absorption filters
Photon detector
Target
Ly-alpha block
121.534nm (H)
121.567nm (D)
・Photon counting
・Imaging
Band-pass filter
Bandpass (115-125nm
Elec.
Optics | Photon correction by Cassegrain-type telescope.
Absorption filters | H Ly-α (121.567nm) blocking, D Ly-α (121.533nm) blocking
Band-pass filter | Elimination of the VIS, UV (Center~120nm, FWHM~10nm).
Photon detector | Conversion from photon to electron signal (I.I.+FOP+CMOS).
Electronics | Power supply for filament and control the photon detector with HV.
photon correction

## Slide 3: Block diagram and specifications
Parameters | Values | Note
Mass, size | <2.5U, <1.75 kg | Inc. baffle, electronics (600g)
FOV | 4.5°x4.5° | 256x256 (spot diagram ~0.02°), 2k x 2k CMOS (5.5um/pix)
Aperture | Φ60 [mm] | Al/MgF2 coating, focal length = 261 [mm] (F/4.35) (TBD)
Ly-α filter | Φ35 [mm], L=40 [mm] | Ly-α (D/H) absorption by resonance scattering, MgF2 (t=1mmx4), T. (total): 10-25% (filament off)
Bandpass filter | Φ25.6 [mm] | Trans.~5% ( <<1% OI130.4 trans.) , FWHM: ~10nm
Effective area | 2x10-3 [cm2] (TBC) | Geometrical: ~5 [cm2] (w/ baffle), Eff.: ~0.007 [cm2], ~0.02 [cps/pix/kR]
Cassegrain-type optics
Absorption filters
Photon detector
Target
photon correction
Ly-alpha block
121.534nm (H)
121.567nm (D)
・Photon counting
・Imaging
Band-pass filter
Bandpass (115-125nm
Elec.

## Slide 4: Optics (Al+MgF2 Mirror) and Bandpass filter
R=65%@121.6nm
Al+MgF2
Al
1st and 2nd mirror (BBM)
Reflectance of sample mirrors. (coatings test)
Sample mirror
Trans.=7~9%
FWHM~10nm
Transmittance of BPF (BBM)
BPFs (lab. Experiment)

## Slide 5: Photon detector (Image Intensifier + FOP +CMOS)
CMOS image (1 flame)
Composite image (50 flames with centroid calc.)
UV
Vis. image
50fps CMOS image
<30,000 counts/flame
50 x 30,000 = 1.5Mcps
x150 (MCP analog system)

## Slide 6: Ly-alpha brightness?
Comet | Period [yr] | B max. [kR] | Norm. B min. [kR] | Norm. B max. [kR]
2P/Encke | 3.3 | 18 | 0.20 | 10.4
46P/Wirtanen | 5.44 | 0.046 | 0.06 | 0.055
103P/HARTLEY2 | 6.47 | 0.15 | 0.003 | 0.003
21P/G-Z | 6.55 | 12.7 | 4.3 | 15.6
67P/C-G | 6.57 | 0.2 | 0.33 | 0.33
1P/Halley | 75.3 | 99.5 | 6.2 | 70.2
Y1/Bennett | 1678 | 40 | 12.5 | 50.2
C/1996 B2 Hyakutake | ~0.11My | 10 | 11.5 | 11.5
C/1995 Hale-Bopp | ~0.90My | 12 | 9.94 | 9.94
P1/Garrardd | N/A | 0.1 | 0.27 | 0.26
E1/Kohoutek | N/A | 500 | 0.62 | 16
C/2013 US10 Catalina | N/A | 100 | 70 | 70
C/1975 V1-A (West) | N/A | 150 | 22.4 | 22.4
Brightness range
  JFC: 0.05~10 kR
  LPC or Hypobaric: 0.5~ 500 kR
HI shall be optimized for 0.5-500k
(note1) IPM Ly-α: 0.2-0.7kR
(note2) D/H ratio: 0.0001~0.001

## Slide 7: Absorption filter
Glass cell filled with H2 (or D2).
H (or D) Lyman-α from the coma can be deduce separately.
Line width (Doppler broadening) can also be deduced.
Fil. temp.
= low
Low temp. target
High temp. target
Fil. temp.
= mid.
Fil. temp.
= high
Fil. power
Photon counts on the detector
High temp. target
Low temp. target
W1
W2
W3
W0
Slope  Temperature

## Slide 8: Observation scenarios
Imaging mode (Cruising)
Light-curve mode (Closest approach)
4°=107km (from 1AU)
FOV(256x256)
Image
(1pix= 5x104km)
coma
HI FOV
1000km
HI FOV
B1 Velocity
Nucleus
105~106km
Light-curve
HI FOV
~2kbps
130kB/image

## Slide 9: Imaging mode (cruising)
Image data specifications
  FOV: 107 km x 107 km (from 1au)
  Spatial resolution: 0.5-1×105 km (from 1au)
  Volume: 135 kB/Image (incl. header)
  Acc. : 1-1000 (TBD) sec/Image
  Obs. Freq.: 0-2(TBD) obs./month
Science targets
  Spatial structures related to…
    Upward/Downward for sun
    Nucleus structure and rotation
    Optical thickness
  H2O production rate
  Heliocentric distance dependence of various parameters.
4°=107km (from 1AU)
FOV(256x256)
coma
130kB/image

## Slide 10: Light-curve (photon counting) mode
D/H ratio
HI FOV
1000km
HI FOV
B1 Velocity
Nucleus
105~106km
HI FOV
Photon counting along the B1 trajectory
H, D filters on/off (cyclically)  D/H ratio.
S/N: ~5 (1P/Halley case, D/H=1e-4)
Count rate along B1 trajectory (ex. v=20km/s, D/H=5E-4)
V = 20km/s
+/-150s obs. at C.A.
90% abs. for H and D filters
(Optically thick for H Ly-a)
baseline
D Cell on
D Cell off
Brightness at 1E5km [R]
SNR, Brightness vs D/H
baseline
1p/Halley
D Cell on
D Cell off

## Slide 11: Development status (BBM activities)
Optical test (BBM)
Test image (iphone12mini)
Electronics functional test (BBM)
HI optics
Cell(s)
Test mirror
CMOS
Test image (through BBM optics)
VT (cell BBM)
Filament
I.I. attachment with FOP and CMOS (GSENSE)
Image Intensifier
3 mm

## Slide 12: Summary
HI on B1 spacecraft
  HI (Hydrogen Imager) will make a Ly-alpha (121.6nm) imaging of comet coma.
Science targets
  Activity of the LPC.
  D/H ratio and H temperature.
Current status
  Basic design (hardware, software) definition.
  Components BBM evaluation.
  Feasibility study for various targets with coma mode calculations.